Software Defined Radio (SDR)
by Scott Hall
TriLUG Presentation
Nov. 10, 2016

---
Background : Radio the Old Way
Simple Mixer Detector :
Creates dual image at twice the « beat » frequency

---
Background : Radio the Old Way
Typical Superhetrodyne Front End :
- Share common characteristic – range of signals is very large
- Chance to encounter two strong closely-spaced signals at same time

---
Background : Radio the Old Way
Typical Superhetrodyne Front End :
- Spacing between signals becomes smaller
- Inter-modulation-generated false signals become likely
- Simple micer produces a mirror image

---
Background : Radio the Old Way
I-Q Quatrature Front End :
- 90-degree phase shift between two identical mixers
- Second phase shift cancels second signal image, selects only desired signal

---
Background : Radio the Old Way
Problems with traditional method :
- Limit cross-functionality
- Can only be modified through physical intervention
- Greater number of hardware parts
- Minimal flexibility in supporting multiple waveform standards
- Higher production costs

---
What is Software Defined Radio ?
 Wikipedia : Software-defined radio (SDR) is a radio communication system where components that have been typically implemented in hardware (e.g. mixers, filters, amplifiers, modulators/demodulators, detectors, etc.) are instead implemented by means of software on a personal computer or embedded system. While the concept of SDR is not new, the rapidly evolving capabilities of digital electronics render practical many processes which used to be only theoretically possible.

---
What is Software Defined Radio ?
 Joe Mitola says, "A software radio is a radio whose channel modulation waveforms are defined in software. That is, waveforms are generated as sampled digital signals, converted from digital to analog via a wideband DAC and then possibly upconverted from IF to RF. The receiver, similarly, employs a wideband Analog to Digital Converter (ADC) that captures all of the channels of the software radio node. The receiver then extracts, downconverts and demodulates the channel waveform using software on a general purpose processor."

---
What is Software Defined Radio ?

---
What is Software Defined Radio ?
Two definitions of Software Radio :
1. Software Controlled Radio: Radio in which some or all of the physical layer functions are Software Controlled. In other words this type of radio only uses software to provide control of the various functions that are fixed within the radio.
2. Software Defined Radio: Radio in which some or all of the physical layer functions are Software Defined. In other words, the software is used to determine the specification of the radio and what it does. If the software within the radio is changed, its performance and function may change.

---
What is Software Defined Radio ?
The essence of the Software Defined Radio, SDR is that it has a generic hardware platform on which software runs to provide functions including modulation and demodulation, filtering (including bandwidth changes), and other functions such as frequency selection and if required frequency hopping. By reconfiguring of changing the software, then the performance or the radio is changed.
To achieve this the software defined radio technology uses software modules that run on a generic hardware platform consisting of digital signal processing (DSP) processors as well as general purpose processors to implement the radio functions to transmit and receive signals.

---
What is Software Defined Radio ?
Ideal Software Radio :
Not only does this form of SDR have full programmability, but it is also able to support a broad range of functions and frequencies at the same time. With many electronic items such as cellphones having many different radios and standards. A software definable multifunction phone would fall into this category.

---
What is Software Defined Radio ?
Typical Software Radio :

---
What is Software Defined Radio ?
Because the signals are processed entirely in digital form inside a computer :
- The hardware required to implement SDR is unbelievably simple
- Performance – considering the sparce hardware requirement – can be as good as any superhet
- It is easier to perform phase modulation/ demodulation as well as amplitude modulation/demodulation

---
What is Software Defined Radio ?
Because the signals are processed entirely in digital form inside a computer :
- All the filtering and signal detection can take place in the digital domain
- An entire range of signals is sampled, able to support a broad range of functions and frequencies at the same time
- Allows simple multimode, multiband and multitrunking

---
What is Software Defined Radio ?
Because the signals are processed entirely in digital form inside a computer :
- Comparatively inexpensive to change, enhance and upgrade
- Can be implemented with hardware help implemented through modifiable software or firmware operating on programmable processing technologies. These devices include field programmable gate arrays (FPGA), digital signal processors (DSP), general purpose processors (GPP), programmable System on Chip (SoC) or other application specific programmable processors

---
What is Software Defined Radio ?
Because the signals are processed entirely in digital form inside a computer :
- Waveform portability – allowing interoperability and obsolelscence mitigation
- Security (and able to update to further security)

---
What is Software Defined Radio ?
Block Diagram of Typical SDR : (see [3])

---
What is Software Defined Radio ?
Block Diagram of Typical DSP :

---
Implementing Software Defined Radio :
Using Raspberry Pi as a Transmitter :
Using Raspberry Pi as a Receiver :

---
Implementing Software Defined Radio :
Using Raspberry Pi with GNU Radio :

---
Implementing Software Defined Radio :
Using Raspberry Pi with GNU Radio :

---
Example Software :

---
Example Software :

---
References :
[1] ARRL: Software Defined Radio
http://www.arrl.org/software-defined-radio
[2] Radio-Electronics.Com: Software Defined Radio, SDR
http://www.radio-electronics.com/info/rf-technology-design/sdr/software-defined-radios-tutorial.php
[3] Software Defined Radio Forum Base Station Working Group Base Station System Structure
http://www.sdrforum.org/pages/documentLibrary/documents/SDRF-01-P-0006-V2_0_0_BaseStation_Systems.pdf
[4] Wireless Innovation Forum: What is Software Defined Radio
http://www.wirelessinnovation.org/assets/documents/SoftwareDefinedRadio.pdf
[5] Electronic Design: The Quest Continues For The SDR Holy Grail
http://electronicdesign.com/communications/quest-continues-sdr-holy-grail

---
Links :
- SDRadio: Playing with your Dongle – An Introduction to Software Defined Radio Using Cheap TV Tuner Cards
     - Justin Rogosky Hack3rcon 4 (Hacking Illustrated Series InfoSec Tutorial Videos)
  http://www.irongeek.com/i.php?page=videos/hack3rcon4/10-sdradio-playing-with-your-dongle-an-introduction-to-software-defined-radio-using-cheap-tv-tuner-cards-justin-rogosky
- Jeff Blaine, ACØC: An Introduction to Software Defined Radios
  http://www.ac0c.com/attachments/An_Introduction_to_Software_Defined_Radios_v2a.pdf
- SDR is the Future: Elektor SDR Receiver
  http://sdrrocks.blogspot.com/2008/04/elektor-sdr-receiver.html
- Elektor SDR Reloaded
  https://www.elektormagazine.com/magazine/elektor-201607/29124
- Elektor SDR Reloaded (150515-91) – Elektor
  https://www.elektor.com/elektor-sdr-reloaded-150515-91

---
Links :
- Dream And Elektor Usb Sdr – Dream
  http://drm.sourceforge.net/wiki/index.php/Dream_And_Elektor_Usb_Sdr
- Elektor Software Defined Radio
  https://www.youtube.com/watch?v=XcSQUQATkxE
- Elektor Software Defined Radio Setup
  https://www.youtube.com/watch?v=XCEA02AvuwE
- Hacking the Wireless World with Software Defined Radio – 2.0
  https://www.youtube.com/watch?v=MKbU3HhG2vk
- Track Aircraft with a $20 Software Defined Radio, Hak5 1525.2
  https://www.youtube.com/watch?v=HS38q3YXsY4
- GSM Sniffing: Voice Decryption 101 - Software Defined Radio Series #11
  https://www.youtube.com/watch?v=krJJKjYdwgc
- GNU Radio
  http://gnuradio.org/